## Slide 1: SDN-Oriented DDoS Blocking Scheme for Botnet-Based Attacks
Antonio LE CALDARE
Edoardo SASSU
Elena SCARSELLI

## Slide 2: How protection works
Server changes the listening address to a new one when is under attack
The connections requests to the old server address are counted
If the number of connection requests of a client, goes above a certain threshold θ, the client is classified as a bot and all its packets are dropped.

## Slide 3: Why Learning Switch
The learning switch is used in order to avoid the re-implementation of L2 switching functionalities in our controller
  Switch will perform also auto-learning functionalities.
For our purposes, this behaviour must be applied only to ARP and ICMP packets
  ARP for enabling packets sending between clients and server;
  ICMP for testing purposes (ping and error messages).
Our model does not include L3 forwarding
  Packet coming from clients and server are forwarded by default to the switch.

## Slide 5: Our Pseudocode
Differences:
Add rules for packets coming from the server to clients.
Packets coming from server need only to be forwarded, then execution can stop after adding the server forwarding rule.

## Slide 6: Our Pseudocode
Differences:
Checking for connection coming from clients to new server address must be done only when protection is enabled.
The dictionary of clients connecitons must be cleared when connection to new server address is detected.

## Slide 7: Implementatio Issues
Execution order of floodlight modules here.
The normal rule (action.normal) does not work for non hybrid switches: mette la regola e manda i pacchetti inditro
Learning switch:
  Add interface to retreive MAC addresses from the learning switch controller
Deleting rules are specified here.
  OFFlowDelete deletes rules matching at least the specified fields;
  OFFlowDeleteStrict deletes the rules that exactly looks like the match you specify.
Testing is done in python using mininet library
Notes: https://floodlight.atlassian.net/wiki/spaces/floodlightcontroller/pages/1343513/How+to+Write+a+Module#HowtoWriteaModule-OrderingModuleswhenProcessingOpenFlowMessages
Per il normal rule, hybrid switch implementano nativamente il livello due e quindi avrebbero fatto arp e switch
Il learning switch
https://floodlight.atlassian.net/wiki/spaces/floodlightcontroller/pages/1343547/How+to+use+OpenFlowJ-Loxigen

## Slide 8: TESTING SYSTEM

## Slide 9: Testing
Semplificaizoni
Dal vecchio server al nuovo server è hardcoded nei client
I bot fanno continuamente richiesta di connessione HTTP al server
I client mandano richieste periodiche
Il server è multithread
Non è possibile vedere l’effetto del Denial of Service
Far vedere la demo